## Slide 1
Raysense
SMART INDIA HACKATHON 2026
PROBLEM STATEMENT TITLE
Adaptive Variable Resolution 2.5D Lidar Mapping
for Dynamic Environment Perception
PROBLEM STATEMENT ID
SIH26053
ORGANISATION
DRDO
THEME
Smart Automation
PS CATEGORY
Software
TEAM ID
ADD FROM PORTAL
TEAM NAME
Raysense
Notes: PRANAVI — 55s. PS ID + DRDO. Then 93% / 11%. PAUSE 3s after "eleven percent".

## Slide 2
Raysense
Adaptive Point-Budget Lidar Perception for UGVs
@SIH Idea submission- Template
2
A FULL SCAN ALREADY MISSES 9 IN 10 DITCHES
A DITCH AND A PATCH YOU NEVER LOOKED AT GIVE THE SAME SIGNAL
OUR ANSWER
A three-state map
OBSERVED
UNKNOWN
CANDIDATE_NEGATIVE
Unknown is never upgraded to “safe”.
Notes: JEEVIKA — 96s. Walk A / B / C. Land on "B and C are identical". Then the three states, then novelty.

## Slide 3
Raysense
TECHNICAL APPROACH
@SIH Idea submission- Template
3
DITCHES DEGRADE QUADRATICALLY · BUMPS ONLY LINEARLY
Δθ ≤ w · hsensor / r²
Python 3.11 · NumPy
Fixed-grid 2.5D map
Replay + live-sensor seam
43 ms / frame · CPU
Notes: NIKITA — 84s. 0.7 m spacing at 10 m, 9 m at 30 m. That is why a 6 m ditch at 30 m is invisible. Then the six steps.

## Slide 4
Raysense
FEASIBILITY AND VIABILITY
@SIH Idea submission- Template
4
EVERY PARAMETER CHOSEN BY SWEEP, NOT BY EYE
IT RUNS TODAY — 103 TESTS, REPRODUCIBLE BIT-FOR-BIT
NO NEW HARDWARE
GROUND TRUTH KNOWN
103 TESTS PASS
HONEST RISKS
73%
precision, not 100% — crest occlusions
0
frames of RELLIS-3D run so far — next step
no
Jetson benchmark — we will not quote one
Notes: NIKITA — 48s. No new hardware, ground truth known. Volunteer all three risks — especially that RELLIS has NOT been run.

## Slide 5
Raysense
IMPACT AND BENEFITS
@SIH Idea submission- Template
5
91% OF DITCHES AT 5% OF THE POINTS · 20× FEWER
THE SPEED LIMIT NOBODY PUBLISHED
Defence UGVs
unmapped ground becomes navigable
Field operators
a ditch does not damage a vehicle — it ends it
Platform designers
a quantified speed ceiling, per sensor
Notes: ANUJ — 66s. Warmest delivery. Three audiences, then land on 23 km/h and PAUSE.

## Slide 6
Raysense
RESEARCH AND REFERENCES
@SIH Idea submission- Template
6
WE DID NOT INVENT ADAPTIVE LIDAR — WE FOUND WHERE IT BREAKS
Ours: a three-state map · the corrected quadratic floor · a range-normalised gap test
REFERENCES
RELLIS-3D
ICRA 2021 · off-road, Ouster OS1-64
NEC Labs
MEMS foveating lidar — Pittaluga et al.
Adaptive LiDAR Scanning
temporal cues, 2025
AEye iDAR / 4Sight
US 11675053 · 11782136 · 11860313
Larson & Trivedi
DTIC ADA561293 — negative obstacles
IEEE ROBIO 2024
sparse 3D lidar, off-road ditches
Notes: PRANAVI — 41s. We cite these BECAUSE the field exists. Close on the three numbers and stop.